## Slide 1
THERMOTWIN · TECHNICAL OVERVIEW
Physics-informed models
for device decisions
Thermoelectric heat flow, imperfect sensors, inverse inference, controls, and next-experiment selection in one reproducible package.
Open-source · CPU-first · conventional solvers remain the reference
Notes: ThermoTwin asks what can be inferred and decided from sparse thermoelectric measurements. Lead with the problem, not the software inventory.
[Sources]
- README.md
[/Sources]

## Slide 2
One transparent chain connects heat flow to decisions
01 · PHYSICS
Energy balances
Four thermal states
Peltier + Joule + conduction
Contacts, exchangers, PWM
RK4 reference + energy checks
02 · OBSERVE
Imperfect sensors
Noise, bias, lag + gaps
Sparse exchanger data
Hidden module-face states
03 · DECIDE
Inference and design
Identify—or reject—parameters
Compare controls + COP
Choose the next experiment
SYNTHETIC EVIDENCE · NOT HARDWARE VALIDATION
2
Notes: Walk left to right. The equations define the state evolution; a virtual test stand hides and corrupts selected states; inference and design operate only on the declared observations. The conventional solver is the numerical reference throughout.
[Sources]
- thermotwin/ROADMAP.md
[/Sources]

## Slide 3
Physics matters most where sensors cannot see
Chart: Reduction versus data-only
| Missing exchanger | Hidden faces | Energy closure
Error reduction | 87.86 | 99.68 | 99.19
Five paired trials · 56 identical noisy rows · six rows missing around turn-off · neither face observed
0.0071 K
Physics-informed
hidden-face RMSE
Data-only: 2.19 K
5 / 5
Trials show all three
primary advantages
No trial discarded
SYNTHETIC EVIDENCE · NOT HARDWARE VALIDATION
3
Notes: The data-only network fits the retained noisy samples slightly better and trains faster. The physics constraint earns its keep on missing readings, completely hidden face temperatures, and the independently assembled first-law audit. The energy equation is a post-training calculation, not an independent physical law.
[Sources]
- thermotwin/FORWARD_RECONSTRUCTION_COMPARISON.md
[/Sources]

## Slide 4
The twin changes engineering decisions—not only curves
INFER
0.251 K/W
Hidden contact resistance
Recovered using only noisy exchanger temperatures; withheld-sensor RMSE is 0.00187 K.
SELECT
81.46%
Lower joint error
Selected 0.8 A, 20 s pulse versus a naive choice after 20 complete nonlinear refits.
STRESS-TEST
55.3%
As-built pass rate
A nominal efficiency winner becomes fragile under the declared virtual manufacturing spread.
SYNTHETIC EVIDENCE · NOT HARDWARE VALIDATION
4
Notes: These examples span diagnosis, experiment design, and robust product screening. The selected-pulse result is also 11.77 percent better than a closer-energy grid control, so the result is not only an energy-budget effect. The 55.3 percent pass rate is intentionally retained as a negative result.
[Sources]
- thermotwin/ENGINEERING_SHOWCASE.md
- thermotwin/NONLINEAR_EXPERIMENT_SELECTION.md
- thermotwin/MATERIAL_GEOMETRY_BAYESIAN_CODESIGN.md
[/Sources]

## Slide 5
The next proof must come from hardware
What is established
• Tested signs, limits, energy identities, and numerics
• Reproducible synthetic comparisons with conventional baselines
• Explicit identifiability, bias, failure, and transfer checks
• 500+ automated tests and passing hosted CI
What remains unproven
• Agreement between the equations and a physical device
• Global identifiability or universal PINN superiority
• Manufacturing capability, real cost, or product performance
• Calibrated neural uncertainty intervals
Next: collect calibrated current, voltage, and temperature data—fit on some complete experiments and predict one held out in its entirety.
SYNTHETIC EVIDENCE · NOT HARDWARE VALIDATION
5
Notes: Close by separating software and synthetic evidence from physical validation. The next claim should quantify model discrepancy on a calibrated test stand, not add complexity to the neural network.
[Sources]
- thermotwin/TECHNICAL_SUMMARY.md
[/Sources]